## Slide 1
BER Automation:
Estimating Building Energy Ratings at Scale Using AI
Environ 2026
Dr. Avinash Nagarajan · Munster Technological University
CIRCUS — Connecting Initiatives for Rural Communities,
Upscaling their Sustainable Energy · Interreg NWE

## Slide 2
The Problem
2 / 10
• Buildings account for 40% of total energy consumption in the EU
– The largest single source of CO₂ in most North-West European countries
• Energy Performance Certificates (EPCs) are the primary tool for communicating a building's energy status
– BER (Ireland) · DPE (France) · Energieausweis (Germany/Austria) · Energielabel (Netherlands)…
• Commissioning an official EPC requires:
– A qualified assessor visiting the property for 1–3 hours
– Specialist certification software
– €150–€500 per property
• This creates a major barrier for:
– Community energy organisations prioritising retrofit across hundreds of homes
– Local authorities conducting large-scale housing stock assessments
– CIRCUS Interreg NWE partners comparing energy performance across 8 countries

## Slide 3
The Opportunity
3 / 10
• Satellite imagery covers virtually every residential address in NWE — at ~9 cm/pixel resolution
• Google Street View provides photographic exterior surveys of most properties
• AI vision models can classify building features from photographs with remarkable reliability
• The energy physics is well-established — the HWB calculation method has been used by practitioners for decades
• All the inputs needed for an energy rating exist in publicly accessible data
→ Can we automate the entire workflow — from postal address to BER rating — using only publicly available data and AI vision?

## Slide 4
What the Tool Does
4 / 10
Input:
• A postal code or street address + country selection
• Nothing else.
Output in under 30 seconds:
• BER band (Irish A1–G as cross-border reference scale)
• Native country EPC band (DPE / Energieausweis / Energielabel / GEAK…)
• Primary energy: kWh/m²/year · CO₂ emissions: kg/year
• Full energy breakdown: transmission, ventilation, solar & internal gains
• Building characteristics: dimensions, floor area, type, era, heating system
• Retrofit comparison: rating after insulation + heating system upgrade
8 Supported Countries
• IE Ireland (BER A1–G)
• FR France (DPE A–G)
• DE Germany (Energieausweis A+–H)
• BE Belgium (EPC A+–F)
• NL Netherlands (Energielabel A++++–G)
• LU Luxembourg (Energiepass A+–G)
• CH Switzerland (GEAK A–G)
• AT Austria (Energieausweis A++–G+)

## Slide 5
The Automated Pipeline
5 / 10
1 GEOCODING
Address → GPS (Google Geocoding API)
2 IMAGE FETCHING
Satellite (zoom 20) + 4× Street View 0°/90°/180°/270°
3 AI BUILDING ANALYSIS
Claude Vision → type, era, storeys, heating system
4 FOOTPRINT EXTRACTION
Claude Vision (primary) + OpenCV cross-validation
5 HWB CALCULATION
Annual energy balance → kWh/m²/yr → BER band
Input: address + country
Output: BER + native EPC + CO₂
• Initial starting point before site visit. Near-zero marginal cost per assessment.
• Confidence gating: if AI confidence < 0.4 the tool uses safe defaults — it never propagates a low-quality guess
• Graceful degradation at every phase: each step has a fallback so one failure does not crash the pipeline

## Slide 6
AI Building Analysis
6 / 10
• Model: Claude Sonnet (Anthropic) — multimodal vision + language
• All 4 street view images sent in one request — model cross-references all angles
– Features visible from only one angle are captured: oil tanks, heat pump units, party walls, flues
• Country-specific architectural knowledge embedded in prompts:
– Ireland / France: look for external oil tanks in rural areas
– Luxembourg / Netherlands: district heating dominant in urban areas
– Germany: heavy external insulation render common post-1980
– Switzerland: triple glazing + heat pumps more common post-2010 (Minergie)
Parameter | Examples
Building type | Detached / Semi-D / Terraced
Construction era | Before 1980 → After 2010
Storeys | 1 / 2 / 3 / 4
Heating system | Oil, gas, heat pump, biomass, district
Confidence | 0.0 – 1.0
Reasoning | Plain-language explanation
Confidence gating: if confidence < 0.4 (building obscured or no Street View coverage), the tool applies safe defaults and shows the user a clear warning. It does not propagate an uncertain AI guess into the energy calculation.

## Slide 7
The Energy Calculation (HWB Method)
7 / 10
• HWB (Heizwärmebedarf) annual heating balance
– ISO 13790 steady-state basis — same standard used by professional EPC tools across Europe
– Ported cell-by-cell from MTU Excel tool (Benjamin Kaiser, January 2025)
• Every country-specific input sourced from authoritative data:
– Heating Degree Days — degreedays.net 2022 data
– Solar irradiance — PHPP climate database
– Primary Energy Factor — each country's national EPBD transposition
– Grid CO₂ intensity — national grid operators (SEAI, RTE, UBA, ELIA, RVO…)
Annual energy balance:
Q_heating = Transmission losses (fabric)
+ Ventilation losses (air exchange)
− Solar gains (passive solar through windows)
− Internal gains (occupants + appliances)
Final energy = Q_heating ÷ System efficiency
(SCOP for heat pumps — can exceed 1.0)
Primary energy = Final energy × PEF (country-specific)
CO₂ = Final energy × Grid emission factor
BER band = lookup( primary energy / floor area )

## Slide 8
CO₂ Across Countries: A Policy Insight
8 / 10
Country | Grid CO₂ (g/kWh) | Heat pump CO₂ reduction vs gas
Switzerland | 29 | ~93%
France | 52 | ~89%
Belgium | 163 | ~72%
Austria | 156 | ~73%
Luxembourg | 197 | ~66%
Ireland | 210 | ~64%
Netherlands | 290 | ~51%
Germany | 385 | ~49%
Same building. Same heat pump. Same SCOP of 3.5.
In France: a heat pump is near-zero-carbon heating today.
In Germany: a heat pump halves CO₂ but is not yet transformational — grid decarbonisation must follow.
For CIRCUS partners advising communities on retrofit priority, this distinction is critical.
Insulation-first strategies may be more immediately effective in high-carbon-grid countries.

## Slide 9
Retrofit Analysis
9 / 10
Example: Pre-1980 Irish detached house on gas boiler — a very common typology in rural Ireland
Scenario | Primary energy | BER band | CO₂
Baseline (pre-1980, gas boiler) | 177.6 kWh/m²/yr | C2 | 31.3 kg/m²/yr
+ Wall insulation (12 cm) + Roof insulation (20 cm) + Triple glazing | ~130 kWh/m²/yr | B3 | ~22.9 kg/m²/yr
+ Switch to air-source heat pump | ~50 kWh/m²/yr | A2 | ~4.3 kg/m²/yr
Total improvement | −72% | C2 → A2 | −86% CO₂
• Built-in before/after comparison — specify insulation thickness, window U-value, heating system swap
• Identifies which homes benefit most from insulation vs heating system change
• Makes the retrofit pathway tangible for homeowners and community energy organisations
• Directly supports national grant scheme (SEAI / equivalent) conversations

## Slide 10
Accuracy, Limitations & What’s Next
10 / 10
Scenario | Expected accuracy
Clear building, good Street View coverage | ±1–2 BER bands
Obscured or limited Street View | ±2–3 BER bands
No Street View coverage (rural) | ±3–4 BER bands
Apartments / multi-unit blocks | Not recommended
Screening tool — not a substitute for official EPC certification
• U-values from Austrian OIB standards — broadly comparable, not Irish Part L exact
• Electricity CO₂ factors from 2022 — grids are decarbonising rapidly
• Validation vs SEAI BER database (400k+ records) — ongoing
What’s Next
→ Validation against SEAI BER database
→ Batch processing for estate-level assessment
→ Regional climate data (county-level HDD for Ireland)
→ DEAP method mode (official Irish methodology)
→ PDF BER-style report generation
Open to collaboration:
• CIRCUS Interreg NWE partners
• SEAI & local authorities
• Environ researchers
Thank you — Questions welcome