## Slide 1
BER Automation:
Estimating Building Energy Ratings at Scale Using AI
Environ 2026
Avinash Nagarajan · Munster Technological University
CIRCUS — Connecting Initiatives for Rural Communities,
Upscaling their Sustainable Energy · Interreg NWE
Notes: Good morning — and thank you for the introduction. My name is Avinash Nagarajan, and I'm presenting work from the CIRCUS Interreg North-West Europe project at Munster Technological University.
What I want to show you today is a tool that can estimate the energy performance of any residential building across eight European countries — using nothing but a postal address, and delivering results in under thirty seconds. I'll walk you through the problem it addresses, how it works, and what it means in practice for communities trying to decarbonise their housing stock.

## Slide 2
The Problem
2 / 10
• Buildings account for 40% of total energy consumption in the EU
– The largest single source of CO₂ in most North-West European countries
• Energy Performance Certificates (EPCs) are the primary tool for communicating a building's energy status
– BER (Ireland) · DPE (France) · Energieausweis (Germany/Austria) · Energielabel (Netherlands)…
• Commissioning an official EPC requires:
– A qualified assessor visiting the property for 1–3 hours
– Specialist certification software
– €150–€500 per property
• This creates a major barrier for:
– Community energy organisations prioritising retrofit across hundreds of homes
– Local authorities conducting large-scale housing stock assessments
– CIRCUS Interreg NWE partners comparing energy performance across 8 countries
Notes: Let me set the scene. Buildings are responsible for roughly forty percent of total energy use in the EU — they are the single largest source of CO₂ in most North-West European countries. Improving the energy performance of existing housing stock is central to the EU's 2050 climate targets and, closer to home, to the ambitions of the CIRCUS project.
The primary tool for this work is the Energy Performance Certificate. These certificates — called a BER in Ireland, a DPE in France, an Energieausweis in Germany and Austria — tell you how energy-efficient a building is and guide retrofit decisions.
The problem is access. Getting an official EPC means paying a qualified assessor to visit the property, conduct a detailed survey, and process it through certification software. In Ireland that costs between €150 and €500 per house, and takes a specialist the better part of a day. For a community energy organisation trying to prioritise retrofit activities across an entire village or townland — usually with limited budgets and volunteer capacity — this is an enormous barrier. You simply cannot afford to pre-assess hundreds of homes before knowing which ones to target.

## Slide 3
The Opportunity
3 / 10
• Satellite imagery covers virtually every residential address in NWE — at ~9 cm/pixel resolution
• Google Street View provides photographic exterior surveys of most properties
• AI vision models can classify building features from photographs with remarkable reliability
• The energy physics is well-established — the HWB calculation method has been used by practitioners for decades
• All the inputs needed for an energy rating exist in publicly accessible data
→ Can we automate the entire workflow — from postal address to BER rating — using only publicly available data and AI vision?
Notes: But here is where it gets interesting. Satellite imagery now covers virtually every residential address in North-West Europe at a resolution that lets you measure a building's footprint. Google Street View provides near-complete photographic coverage of residential streets — effectively giving you an exterior survey of most properties without ever visiting them. Modern AI vision models can examine those photographs and make reliable inferences about when a building was constructed, what type it is, and what heating system it likely uses. And the energy calculation itself is not new — the HWB annual balance method has been used by practitioners for decades.
So we had all the ingredients: imagery, AI, and a well-established calculation method. The question was simply whether we could connect them into a fully automated pipeline — from postal code to BER rating, at scale, at near-zero marginal cost.

## Slide 4
What the Tool Does
4 / 10
Input:
• A postal code or street address + country selection
• Nothing else.
Output in under 30 seconds:
• BER band (Irish A1–G as cross-border reference scale)
• Native country EPC band (DPE / Energieausweis / Energielabel / GEAK…)
• Primary energy: kWh/m²/year · CO₂ emissions: kg/year
• Full energy breakdown: transmission, ventilation, solar & internal gains
• Building characteristics: dimensions, floor area, type, era, heating system
• Retrofit comparison: rating after insulation + heating system upgrade
8 Supported Countries
• IE Ireland (BER A1–G)
• FR France (DPE A–G)
• DE Germany (Energieausweis A+–H)
• BE Belgium (EPC A+–F)
• NL Netherlands (Energielabel A++++–G)
• LU Luxembourg (Energiepass A+–G)
• CH Switzerland (GEAK A–G)
• AT Austria (Energieausweis A++–G+)
Notes: The answer is yes — and this is what it looks like in practice. You open a browser, type in a postal code or street address, select the country, and click run. That is the entire user interaction required.
Within about thirty seconds, the tool returns a full building energy profile. You get the BER band on the Irish scale — which we use as a consistent cross-border reference for the CIRCUS programme — alongside the native EPC format that residents in each country would actually recognise on their own national certificate. You get primary energy in kilowatt-hours per square metre per year, annual CO₂ emissions, a breakdown of where energy is being lost, and the building's physical characteristics as estimated by the AI. And you get a retrofit comparison: what would the rating become if you added insulation or switched to a heat pump?
The tool covers all eight partner countries of the CIRCUS Interreg NWE programme — Ireland, France, Germany, Belgium, the Netherlands, Luxembourg, Switzerland, and Austria. No specialist knowledge is required to operate it. A community energy officer or local authority staff member can run it directly.

## Slide 5
The Automated Pipeline
5 / 10
1 GEOCODING
Address → GPS (Google Geocoding API)
2 IMAGE FETCHING
Satellite (zoom 20) + 4× Street View 0°/90°/180°/270°
3 AI BUILDING ANALYSIS
Claude Vision → type, era, storeys, heating system
4 FOOTPRINT EXTRACTION
Claude Vision (primary) + OpenCV cross-validation
5 HWB CALCULATION
Annual energy balance → kWh/m²/yr → BER band
Input: address + country
Output: BER + native EPC + CO₂
• Initial starting point before site visit. Near-zero marginal cost per assessment.
• Confidence gating: if AI confidence < 0.4 the tool uses safe defaults — it never propagates a low-quality guess
• Graceful degradation at every phase: each step has a fallback so one failure does not crash the pipeline
Notes: Let me walk through the pipeline, because the engineering decisions are worth understanding.
Phase one is geocoding — the address is converted to GPS coordinates using the Google Geocoding API, with a country filter applied to ensure we stay within the right borders.
Phase two fetches imagery. A satellite image at zoom level twenty gives us a top-down view of the building at roughly nine centimetres per pixel. For Street View, rather than using a fixed compass direction, the tool queries the Street View metadata API to find where the nearest camera physically was, computes the geodesic bearing from that camera to the building, and then fetches four images at ninety-degree intervals around that bearing. The building is centred in every photograph, and we capture the full exterior — front, right, rear, and left.
Phase three sends all four images simultaneously to Claude Sonnet, Anthropic's AI vision model, along with a detailed country-specific prompt. Claude returns its assessment of building type, construction era, storeys, heating system, and a confidence score.
Phase four extracts the building's footprint from the satellite image — also using Claude Vision, with the map scale in metres per pixel injected into the prompt so it can reason in real-world dimensions. An independent OpenCV algorithm runs in parallel as a cross-validation check. If both methods agree within thirty percent, confidence is boosted; if they disagree, the AI result is trusted; if the AI fails entirely, OpenCV acts as fallback.
Phase five runs the energy calculation — which I will explain on the next slide.

## Slide 6
AI Building Analysis
6 / 10
• Model: Claude Sonnet (Anthropic) — multimodal vision + language
• All 4 street view images sent in one request — model cross-references all angles
– Features visible from only one angle are captured: oil tanks, heat pump units, party walls, flues
• Country-specific architectural knowledge embedded in prompts:
– Ireland / France: look for external oil tanks in rural areas
– Luxembourg / Netherlands: district heating dominant in urban areas
– Germany: heavy external insulation render common post-1980
– Switzerland: triple glazing + heat pumps more common post-2010 (Minergie)
Parameter | Examples
Building type | Detached / Semi-D / Terraced
Construction era | Before 1980 → After 2010
Storeys | 1 / 2 / 3 / 4
Heating system | Oil, gas, heat pump, biomass, district
Confidence | 0.0 – 1.0
Reasoning | Plain-language explanation
Confidence gating: if confidence < 0.4 (building obscured or no Street View coverage), the tool applies safe defaults and shows the user a clear warning. It does not propagate an uncertain AI guess into the energy calculation.
Notes: The building analysis phase is where the AI does the heavy lifting, and a few design decisions here are particularly important.
Sending all four street view images in one request means the model can cross-reference them. An oil tank visible only from the rear, a heat pump unit on the side wall, a shared party wall only apparent from the left — the model picks all of these up when it has a complete exterior survey, rather than making inferences from a single front-facing photograph.
We have also embedded country-specific architectural knowledge directly into the prompts. The visual signatures of construction eras differ significantly between countries — a 1980s German building with heavy external insulation render looks nothing like a 1980s Irish cavity-wall semi-detached. Rural Irish and French properties are far more likely to have oil storage tanks. District heating is common in Luxembourg and the Netherlands but rare in rural Ireland. This localisation meaningfully improves classification accuracy across all eight countries.
The confidence gating is a critical safeguard. The model returns a confidence score with every analysis. If that score falls below 0.4 — the building is obscured by vegetation, or there is simply no Street View coverage at that address — the tool does not use the uncertain classification. It applies conservative defaults and displays a clear warning to the user. We would rather give an honest, conservative default than propagate a low-quality AI guess through to the final energy figure.

## Slide 7
The Energy Calculation (HWB Method)
7 / 10
• HWB (Heizwärmebedarf) annual heating balance
– ISO 13790 steady-state basis — same standard used by professional EPC tools across Europe
– Ported cell-by-cell from MTU Excel tool (Benjamin Kaiser, January 2025)
• Every country-specific input sourced from authoritative data:
– Heating Degree Days — degreedays.net 2022 data
– Solar irradiance — PHPP climate database
– Primary Energy Factor — each country's national EPBD transposition
– Grid CO₂ intensity — national grid operators (SEAI, RTE, UBA, ELIA, RVO…)
Annual energy balance:
Q_heating = Transmission losses (fabric)
+ Ventilation losses (air exchange)
− Solar gains (passive solar through windows)
− Internal gains (occupants + appliances)
Final energy = Q_heating ÷ System efficiency
(SCOP for heat pumps — can exceed 1.0)
Primary energy = Final energy × PEF (country-specific)
CO₂ = Final energy × Grid emission factor
BER band = lookup( primary energy / floor area )
Notes: The energy calculation uses the HWB annual heating balance — Heizwärmebedarf in German, meaning heating energy requirement. This is a steady-state annual method based on ISO 13790, the same standard that underpins professional EPC calculation tools across Europe. It was ported cell by cell from an Excel workbook developed by Benjamin Kaiser at MTU in January 2025.
The balance is straightforward: heating demand equals transmission losses through the building fabric plus ventilation losses from air exchange, minus usable solar gains through glazing and internal heat from occupants and appliances. That heating demand is divided by the heating system efficiency — or the seasonal coefficient of performance for heat pumps, which can exceed 1.0 because heat pumps extract free environmental energy — to give final energy consumption. Final energy is then multiplied by a country-specific Primary Energy Factor to get primary energy, which determines the EPC band.
Every country-specific input comes from authoritative sources: heating degree days from degreedays.net, solar irradiance from the Passive House Planning Package climate database, primary energy factors from each country's national EPBD transposition, and grid carbon intensity from national grid operators. The same physical building in different countries produces a genuinely different calculation — not just a different label.

## Slide 8
CO₂ Across Countries: A Policy Insight
8 / 10
Country | Grid CO₂ (g/kWh) | Heat pump CO₂ reduction vs gas
Switzerland | 29 | ~93%
France | 52 | ~89%
Belgium | 163 | ~72%
Austria | 156 | ~73%
Luxembourg | 197 | ~66%
Ireland | 210 | ~64%
Netherlands | 290 | ~51%
Germany | 385 | ~49%
Same building. Same heat pump. Same SCOP of 3.5.
In France: a heat pump is near-zero-carbon heating today.
In Germany: a heat pump halves CO₂ but is not yet transformational — grid decarbonisation must follow.
For CIRCUS partners advising communities on retrofit priority, this distinction is critical.
Insulation-first strategies may be more immediately effective in high-carbon-grid countries.
Notes: This is the slide I want you to pause on, because I think it carries the most important policy implication of everything I am showing you today.
We know that heat pumps are central to retrofit strategies across Europe. But what we often miss is that installing a heat pump produces very different CO₂ outcomes depending on where you are — because the carbon intensity of the electricity grid varies enormously between countries.
Switzerland's grid runs on hydropower and nuclear, producing just twenty-nine grams of CO₂ per kilowatt-hour. France's nuclear-heavy grid sits at fifty-two grams. At the other end, Germany's coal and gas mix emits three hundred and eighty-five grams per kilowatt-hour — more than thirteen times Switzerland's figure.
What does this mean in practice? Install an air-source heat pump with a seasonal COP of 3.5 in a French home, and you cut CO₂ by roughly eighty-nine percent compared to a gas boiler. The same heat pump in Germany cuts CO₂ by about forty-nine percent — still significant, but not transformational, and only until Germany's grid catches up.
For CIRCUS partners advising communities on where to focus retrofit resources, this distinction is critical. In France and Switzerland, pushing hard on heat pump uptake makes sense right now. In Germany and the Netherlands, an insulation-first strategy may deliver more immediate CO₂ benefit, with heat pumps becoming progressively more powerful as the grid decarbonises. The tool makes this visible, by country, for every assessment it runs.

## Slide 9
Retrofit Analysis
9 / 10
Example: Pre-1980 Irish detached house on gas boiler — a very common typology in rural Ireland
Scenario | Primary energy | BER band | CO₂
Baseline (pre-1980, gas boiler) | 177.6 kWh/m²/yr | C2 | 31.3 kg/m²/yr
+ Wall insulation (12 cm) + Roof insulation (20 cm) + Triple glazing | ~130 kWh/m²/yr | B3 | ~22.9 kg/m²/yr
+ Switch to air-source heat pump | ~50 kWh/m²/yr | A2 | ~4.3 kg/m²/yr
Total improvement | −72% | C2 → A2 | −86% CO₂
• Built-in before/after comparison — specify insulation thickness, window U-value, heating system swap
• Identifies which homes benefit most from insulation vs heating system change
• Makes the retrofit pathway tangible for homeowners and community energy organisations
• Directly supports national grant scheme (SEAI / equivalent) conversations
Notes: The retrofit analysis capability is what makes the tool actionable rather than just descriptive.
For any building assessed through the pipeline, you can specify a retrofit package — wall and roof insulation thickness, a target window U-value, and whether to switch the heating system — and the tool recalculates the BER side by side with the current rating.
The example here is a pre-1980 detached Irish house on a gas boiler — one of the most common and most energy-intensive typologies in rural Ireland. Its baseline sits at C2, at 177.6 kilowatt-hours per square metre per year. Add wall and roof insulation plus triple-glazed windows, and it moves to B3 — a twenty-seven percent reduction in CO₂. Add a heat pump on top of that, and it reaches A2 — an eighty-six percent cut in CO₂ compared to the unimproved baseline.
For a community energy officer running a public meeting, this tool lets them pull up any address, show the estimated current rating, and immediately demonstrate what is achievable with a standard deep retrofit package. It makes the pathway to an A-rated home tangible and evidence-based for homeowners who may never have seen their building's energy profile before. That is a powerful engagement tool.

## Slide 10
Accuracy, Limitations & What’s Next
10 / 10
Scenario | Expected accuracy
Clear building, good Street View coverage | ±1–2 BER bands
Obscured or limited Street View | ±2–3 BER bands
No Street View coverage (rural) | ±3–4 BER bands
Apartments / multi-unit blocks | Not recommended
Screening tool — not a substitute for official EPC certification
• U-values from Austrian OIB standards — broadly comparable, not Irish Part L exact
• Electricity CO₂ factors from 2022 — grids are decarbonising rapidly
• Validation vs SEAI BER database (400k+ records) — ongoing
What’s Next
→ Validation against SEAI BER database
→ Batch processing for estate-level assessment
→ Regional climate data (county-level HDD for Ireland)
→ DEAP method mode (official Irish methodology)
→ PDF BER-style report generation
Open to collaboration:
• CIRCUS Interreg NWE partners
• SEAI & local authorities
• Environ researchers
Thank you — Questions welcome
Notes: I want to be transparent about what the tool is and what it is not.
For a building with good Street View coverage and a clearly visible facade, we expect agreement within one to two BER bands of an official assessment — which is a useful and actionable level of accuracy for screening purposes. That widens to two to three bands for partially obscured buildings, and three to four bands for rural properties with no Street View coverage at all.
This is intentionally a screening and prioritisation tool. It should not be used as a substitute for an official EPC where one is legally required — property transactions, building regulations compliance, green finance products. For those purposes, a qualified assessor must conduct a formal assessment. But for identifying where the worst-performing homes are in a community, preparing evidence for funding applications, or showing homeowners their retrofit pathway — this is exactly the right level of detail.
On next steps: we are currently validating the tool against the SEAI BER certificate database, which contains over four hundred thousand rated Irish properties. That will allow us to quantify systematic biases and calibrate confidence across different building typologies. We are also developing batch processing so community organisations can upload a list of addresses and receive assessments in bulk.
Most importantly, we are actively looking for collaboration — with CIRCUS partners across all eight countries, with SEAI, with local authorities, and with researchers in this room. If any of that connects with your work, I would very much welcome a conversation afterwards. Thank you.