## Slide 1: BER Automation: Estimating Building Energy Ratings at Scale Using AI
Avinash Nagarajan | Munster Technological University
CIRCUS Interreg North-West Europe Programme
Environ 2026
Notes: Good morning. My name is Avinash Nagarajan, representing the CIRCUS Interreg North-West Europe project at Munster Technological University. Today, I am excited to demonstrate a novel open-source tool that estimates the energy performance of residential buildings across eight European countries in under 30 seconds—using only a postal address. I will walk you through the AI pipeline powering this tool and discuss how it addresses the critical challenge of decarbonising our housing stock at scale.

## Slide 2: The Challenge of Scale
• Buildings consume 40% of total energy in the EU.
• Energy Performance Certificates (EPCs / BERs) are essential for targeting retrofits.
• The Bottleneck:
  - Official EPCs require a 1–3 hour site visit.
  - Costs range from €150 to €500 per property.
• Impact: Community groups cannot afford to pre-assess entire neighbourhoods.
Notes: To set the scene: buildings are responsible for roughly forty percent of all energy consumption in the EU. If we are to meet our 2050 climate targets, mass retrofitting is non-negotiable. The primary tool we have to guide this is the Energy Performance Certificate. The problem is scalability. Generating an official EPC requires a qualified assessor to physically visit the property, which costs hundreds of euros per house. For a community energy organisation trying to prioritise which homes in a village need the most urgent help, this cost is prohibitive.

## Slide 3: An Automated, AI-Driven Solution
• Concept: Automate the physical survey using public data.
• The Ingredients:
  - Ubiquitous satellite imagery (building footprint).
  - Google Street View (exterior photographic survey).
  - Claude 3.5 Sonnet (visual feature extraction).
  - Proven energy physics (Austrian HWB method).
• Result: Automated pipeline for comprehensive energy profiles.
Notes: The solution lies in combining ubiquitous geospatial data with breakthroughs in AI. Every address in North-West Europe is visible via high-resolution satellite imagery, and Google Street View provides a comprehensive exterior survey. By passing these images to a multimodal AI like Claude 3.5 Sonnet, we can automate the visual inspection phase. We then feed those parameters into a established thermal calculation engine based on the Austrian HWB method.

## Slide 4: The Pipeline Architecture
• Phase 1: Geocoding (Address → GPS)
• Phase 2: Imagery (Satellite + 4x Street View Angles)
• Phase 3: AI Survey (Claude 3.5 Cross-Referencing)
• Phase 4: Footprint (AI Primary + OpenCV Fallback)
• Phase 5: Thermal Engine (HWB Annual Balance)
Notes: Let’s look under the hood. Phase 1 geocodes the address. Phase 2 fetches imagery. Crucially, we fetch four Street View images at 90-degree intervals, giving us a 360-degree exterior survey. In Phase 3, the AI analyses these images. Phase 4 extracts dimensions from the satellite view. Finally, Phase 5 runs the thermal physics calculation to determine energy demand and CO2 emissions.

## Slide 5: Advanced AI Vision & Confidence Gating
• Multi-Angle Cross-Referencing: 4 views sent in one request.
• Detects hidden features (heat pumps, oil tanks, party walls).
• Country-Specific Prompts: Adapts to local typologies.
• Confidence Gating: If confidence < 0.4, use safe defaults.
Notes: The most powerful aspect is multi-angle cross-referencing. By sending all four images to Claude simultaneously, the model acts like a human surveyor walking around the property. It might spot an oil tank at the back or a heat pump on the side. We implemented Confidence Gating: if the building is obscured and the AI confidence is below 0.4, we fallback to conservative defaults to avoid hallucinations.

## Slide 6: Dual-Method Footprint Extraction
• Primary: Claude Vision (Context-Aware)
  - Receives GPS scale (m/pixel).
  - Measures single units in terraced rows.
• Secondary: OpenCV (Algorithmic)
  - Canny edge detection + contour scoring.
• Reconciliation: Both must agree within 30% for high confidence.
Notes: Extracting building dimensions from satellite images is difficult. We use a dual-method approach. Our primary engine is Claude Vision, which is context-aware—if it knows a building is part of a terrace, it measures just one unit. As a safety net, we run an independent OpenCV algorithm. If they agree within 30%, we boost confidence. If they disagree, we trust the AI, with OpenCV as a robust fallback.

## Slide 7: The Thermal Calculation Engine
• Method: HWB (Heizwärmebedarf) annual balance.
• Equation: (Losses: Trans. + Vent.) – (Gains: Solar + Int.)
• Localised Data:
  - Heating Degree Days (winter severity).
  - Solar irradiance by orientation.
  - National Primary Energy Factors (PEF).
Notes: The thermal engine uses the Austrian HWB method, based on ISO 13790. It is an annual energy balance: losses through fabric and ventilation minus gains from sun and occupants. We divide this by efficiency to get final energy. Every input is localised: we use specific climate data and national Primary Energy Factors for all eight supported countries.

## Slide 8: Cross-Border Policy Insights: Grid CO2
• Grid CO2 Intensity (g/kWh): CH: 29 | FR: 52 | IE: 210 | DE: 385
• Heat Pump CO2 Reduction vs. Gas Boiler:
  - France: ~89% reduction
  - Germany: ~49% reduction
• Takeaway: Retrofit strategy must follow grid decarbonisation.
Notes: The tool surfaces critical policy insights. The impact of a heat pump depends on the local grid. In France, with low-carbon nuclear, a heat pump cuts emissions by 90%. In Germany, with a higher carbon mix, it cuts emissions by about 50%. For community groups, this means localized strategy is vital: in coal-heavy grids, insulation might be the first priority while the grid decarbonises.

## Slide 9: Actionable Retrofit Pathways
• Example: Pre-1980 Detached House (Ireland)
  - Baseline: C2 (177 kWh/m²/yr)
  - Step 1: Insulation + Triple Glazing → B3
  - Step 2: Switch to Heat Pump → A2
• Result: 86% total CO2 reduction.
• Utility: Shows residents a tangible path to an A-rating.
Notes: The tool is designed to be actionable. Take a typical pre-1980 Irish house on gas. It starts at C2. Add insulation and triple glazing, it jumps to B3. Add a heat pump, it reaches A2—an 86% carbon reduction. Energy officers can show residents the exact pathway required to transform their specific home.

## Slide 10: Validation & Next Steps
• Accuracy: ±1–2 bands (with good Street View).
• Validation: Cross-referencing 400,000 SEAI certificates.
• Roadmap:
  - Irish DEAP methodology implementation.
  - Batch processing for estate-level uploads.
• Open Source: Collaborate with CIRCUS & MTU.
Notes: To conclude, this is a screening tool, not an official EPC. We are currently validating it against 400,000 official Irish certificates to fine-tune our models. Future steps include implementing the official DEAP method and bulk processing. The code is open source and we are looking for collaboration. Thank you.